Comparing Flavors of TCP on Different Network Topologies
By: Louie DiBernardo

---
How is everything setup?
- Mininet running natively on an ubuntu installation on Linux 5.13.0-39-generic and on MPTCP version as well.
- As a controller, I have a second ubuntu installation running OpenDayLight.
- Currently both run directly on hardware, not VMs

---
Fat Tree Topology - Visualizer
Using Spear Narmox visualizer:

---
Leafspine Topology
Using Spear Narmox visualizer:

---
Superspine Topology
Using Spear Narmox visualizer:

---
Fat Tree Topology – Visualizer: ODL
Interestingly, ODL has some limits to its DLUX package visualizer.

---
Leaf spine Topology – Visualizer: ODL
Interestingly, ODL has some limits to its DLUX package visualizer.

---
Super spine Topology – Visualizer: ODL
Interestingly, ODL has some limits to its DLUX package visualizer.

---
MPTCP Graphs

---
Current Problems
- A lot of issues trying to get the dctcp linux kernel installed, not much documentation seems to exist for installing it (at least that I can find)
- TCP and STCP implementations were incorrect! I found this out when merging the graphs together with MPTCP. Currently in the process of testing TCP, will need to figure out path for STCP moving forward.

---
Reproducability
Currently, everything is running hardware, not vm’s. To reporoduce my work (as I currently have it setup) two different computers will need to be running, one with ODL, and one with mininet.

---
Questions?